## Slide 1: Training Volunteers
The ARRL
Introduction to Emergency Communication Course
EC-001 (2011)
Session Four
Notes: Make sure you have modified the Name and Date.
Display this screen as students are arriving for class.

## Slide 2: Reminder
Complete two DHS/FEMA Courses
    IS-100.b Introduction to ICS
    IS-700 National Incident Management System
      Http://training.fema.gov/IS/NIMS.asp
Notes: ARRL conditions!
The two ICS courses must be complete before taking the final exam.

## Slide 3: Session Four Topic
Session 1 – Topics 1, 2, 3, 4, 5a, 5b
Session 2 – Topics 6, 7a, 7b, 7c, 7d, 8, 9, 10
Session 3 – Topics 11, 12, 13, 14, 15
Session 4 – Topics 16, 17, 18, 19, 20
Session 5 – Topics 21, 22, 23, 24, 25, 26, 27
Session 6 – Topics 28, 29, Summary, Final Exam
Notes: The course requires a total of 18 hours.
If a student misses one class they can take a practice quiz for each lesson missed.
A student missing two sessions will be asked to take the course again.
A student missing the last session must wait for the next class and attend the final session for taking the exam again.
An exception would be two Field Examiners agreeing to give the exam at a mutually scheduled time.

## Slide 4: Topic 18 – Equipment Choices for Emergency Communication

## Slide 5
There is no one "best" set of equipment that will
ensure success for every assignment

## Slide 6: January 1, 2013
“When Deployed” for PS or emergencies
Expected outer garment
Standardized look for ARES
Easily Recognized
ID Requirements of NIMS
Waivers granted by SEC

## Slide 7: Professionalism

## Slide 8: Standardized Outer Garment
Safety Green (yellow)
Sliver Reflective Tape
Black Letters on back & black LOGO
ID Badge
Can add organizational name on back in 1” letters or front in ½” letters under the LOGO

## Slide 9: Transceivers - VHF/UHF
Dual band (2m, 440MHz) FM mobile transceiver
  35-50 watt
  Rugged and reliable
  Can operate at reasonably high duty cycles
    An external cooling fan if one is not built-in
Handheld transceivers used only when:
  Extreme portability is needed
    "shadowing" an official
  Adequate battery or other DC power is not available
  Should not be relied upon to operate with a high duty-cycle at maximum power
    They can overheat and fail
Notes: some models allow simultaneous reception on more than one frequency on the same band
Some mobiles have separate external speaker outputs for each band. For high traffic locations, such as a Net Control or Emergency Operations Center, a separate radio for each net is a better choice since it allows both to be used simultaneously by different operators. (Antennas must be adequately separated to avoid "de-sensing.")
Many dual-band transceivers also offer a "cross-band repeater" function, useful for linking local portables with distant repeaters, or as a quickly deployable hill-top repeater. True repeater operation is only possible if all other mobile and portable stations have true dual-band radios. Some so-called "dual" or "twin" band radios do not allow simultaneous or cross-band operation -- read the specifications carefully before you purchase one.

## Slide 10: Transceivers - HF
Having both AC and DC power capability
12 Volt HF radios
  100 watt
  QRP (less than 5 watts)
100 watt variable output radios should be used
  Unless power consumption is extremely important
  Overcome noise at the receiving station by using high power
  Turn it down to conserve battery power when necessary
Do not use DC to AC inverters to power HF radios
Notes: Most use a high-frequency conversion process that generates significant broad-spectrum RF noise at HF frequencies that is difficult to suppress. Direct DC powering is more efficient in any case.

## Slide 11: Voltage Tolerance
12 Volts DC
13.0 to 13.8 Volts DC
11.5 to 15 Volts DC
Transmit vs. Receive

## Slide 12: Radio Receiver Performance
Sensitivity
  Ability to receive weak signals
Selectivity
  Ability to reject signals on adjacent frequencies
Intermodulation rejection
  Ability to prevent undesired signals from mixing within the receiver and causing interference
  Important when operating near public service and business radio transmitters

## Slide 13: Radio Receiver Performance (cont)
Receiver filters
  Important for effective HF operation.
  Choose appropriate filters for the types of operations you are most likely to use, including CW, RTTY, and phone
Digital Signal Processing (DSP)
  Can allow clear reception of signals that might not otherwise be possible in situations with heavy interference

## Slide 14: Radio Receiver Performance (cont)
"Noise blankers"
  Reduce impulse noise from arcing power lines, vehicle and generator ignition systems, and various other sources

## Slide 15: VHF/UHF Antennas
Good antenna, mounted as high as possible, is more important than high transmitter power
  Provides gain to both the transmitter and receiver
  Higher gain antenna may also allow output power to be reduced
    Prolonging battery life
Flat terrain (Phoenix, not Seattle)
  Use a mast-mounted single or dual-band antenna with at least 3dBd gain

## Slide 16: VHF/UHF Antennas (cont)
Operating in a valley
  Use a low or "unity" gain antennas that have "fatter" radiation lobes
    Unity gain J-poles
  Gain antenna = low angle of radiation
Directional 2m coverage
  Three or four element Yagi-Uda array (7dB gain)
  2-way colinear antenna,
    "Stationmaster" series
  Commercial open dipole array antennas

## Slide 17: VHF/UHF Antennas (cont)
Magnetic mount mobile antenna
  Operating in someone else's vehicle
  Can also be used indoors
    Sticking them to any steel surface, such as filing cabinets, beams, or ductwork, even up-side down
Rubber duckies
  Negative gain
  Use at least a ¼ wave flexible antenna
  Telescoping 5/8 wave antenna for long-range use

## Slide 18: VHF/UHF Antennas (cont)
“Roll-up J-pole" antennas
  Made from 300 ohm television twin-lead wire
  Can be tacked up on a wall or hoisted into a tree with heavy-duty string

## Slide 19: HF Antennas
No single perfect antenna for HF operation
  Depends on:
    Size and terrain of the area you need to cover
    Conditions under which you must install/use it
“Near Vertical Incidence Skywave" (NVIS)
  For local operations up to a few hundred miles
  Random wire or dipole hung at a less than ¼ wavelength above the ground
  Signal is reflected almost straight up, bounces off the ionosphere directly back downward
  Best on 40 meters during the day, switching to 80 meters around sunset

## Slide 20: NVIS

## Slide 21: NVIS (cont)

## Slide 22: HF Antennas
Antenna tuner is necessary for most portable wire antennas
  Especially for NVIS antennas
  Antenna's impedance varies with height above ground and proximity to nearby objects
    Can be a real problem with expedient installations
Include a ground rod, clamps and cable in your kit since almost all radios and tuners require a proper ground in order to work efficiently

## Slide 23: HF Antennas (cont)
Communication beyond 200 miles
  Commercial trapped vertical may work
    No ability to reject interfering signals from other directions
  Directional (beam) antennas
    Best performance for very wide area nets on 10 to 20 meters
      Maximize desired signals and reduce interference from stations in other directions
    Expensive, large, and difficult to store and transport

## Slide 24: HF Beam Antenna

## Slide 25: Feedline
VHF and UHF
  Low-loss foam dielectric coaxial cable
    RG-8X or RG-213
HF
  Coaxial cable
  Commercial insulated "ladder" line
Notes: RG-8X is an "in-between" size that offers less loss and greater power handling capability than RG-58 with far less bulk than RG-213. If you with to carry only one type of cable, RG-8X is the best choice.
Ladder line offers somewhat lower loss but more care must be taken in it's routing, especially in proximity to metal objects, or where people might touch it. Coaxial cable is much less susceptible to problems induced by routing near metal objects or other cables.

## Slide 26: Operating Accessories
Headphones
  EOC where multiple radios are in use must use headsets
VOX (voice operated transmit) capability
  Should always be turned off and manual "push-to-talk" buttons used
Desk or boom microphone and foot switch to key the transmitter
Notes: Accidental transmissions caused by background noise and conversations can interrupt critical communications on the net.

## Slide 27: Batteries
Battery power is critical
Match the maximum load of the equipment, and the length of time that operation must continue before they can be recharged
Handheld transceivers
  NiMH batteries
    Store somewhat more energy than NiCd batteries for their size
  Lithium Ion (LIon) batteries
    Much higher power densities, without the so-called "memory effect" of NiCds
Notes: AC power cannot usually be relied upon for any purpose, and portable operation for extended periods is common.

## Slide 28: Batteries (cont)
Optional AA alkaline battery cases
  Recommended emcomm accessory
  Common alkaline batteries
    Somewhat higher power density than NiCd batteries
    Readily available in most store
    May be all you have if you cannot recharge your other batteries.
External 13.8VDC power connection
  Cigarette lighter or external battery use

## Slide 29: Batteries (cont)
External batteries
  Any type can be used with a handheld
  12-15 volt gel cells
  Some battery packs intended for power tools and camcorders
Build a DC power cable for each of your radios, with suitable adapters for each battery type you might use

## Slide 30: Lead Acid Batteries
Flooded (wet)
  Can spill if tipped
SLA (Sealed Lead-Acid)
  Can be operated in any position -- even up-side down
  The optimum charging voltage for 12-volt lead acid batteries should be about two volts more than the battery's rated voltage.

## Slide 31: "Deep-cycle" Batteries
Better choice than common automotive (cranking) batteries
  Not designed to provide consistent power for prolonged periods
Best choice
  Specified for UPS (uninterruptible power source) or recreational vehicle (RV) use

## Slide 32: Sealed Lead Acid (SLA)
Available in smaller sizes that are somewhat lighter
Typical small sizes are 2, 4, and 7Ah, but many sizes of up to more than 100Ah are available
Should never be deeply discharged
  A 12 volt SLA battery will be damaged if allowed to drop below 10.5 volts
Excessive heat or cold can damage SLA batteries
  Storage temperatures between 40 and 60 degrees will provide maximum battery life

## Slide 33: Battery "Power Budgeting”
Busy net control station = transmit current will be the determining factor because of the high duty cycle
Low activity stations = receiver current will dominate

## Slide 34: Chargers, Generators and Solar Power
NiCd and NiMH batteries
  Type of charger required depends on the battery
  “Universal" chargers
  Rapid-rate charger
    Rapid charging can shorten a battery's overall lifespan
Lead-acid batteries
  Always consult the battery's manufacturer for precise charging and maintenance instructions
  Best to slow-charge all batteries
  Automotive and deep cycle batteries can be charged with an automobile and jumper cables, an automotive battery charger, or any constant-voltage source

## Slide 35: Chargers, Generators and Solar Power
SLA or "gel- cell"
  Must be charged slowly and carefully to avoid damage
  Charging voltage must be kept between 13.8 and 14.5 volts
  Keep the charging current level to no more than 1/3 its rated capacity
  Time it takes for a SLA battery to recharge completely will depend on the amount of charge remaining in the battery

## Slide 36: Generators
Required at command posts and shelters
  Lighting, food preparation, and other equipment
Radio equipment can be operated from the same or a separate generator,
  But be sure that co-located multiple generators are bonded with a common ground system for safety
Not all generators have adequate voltage regulation
A voltmeter should be part of your equipment

## Slide 37: Generators (cont)

## Slide 38: Generators (cont)
Noise levels can be a concern
  Placing the generator at a greater distance and using heavier power cables to compensate.
  Can also prevent fumes from entering the building and causing carbon monoxide poisoning
High quality surge suppressors, line voltage regulators, and power conditioners may help protect your equipment from defective generators
Variable voltage transformers ("Variacs" ™) can be useful to compensate for varying power conditions

## Slide 39: Generator Safety

## Slide 40: Power Connectors and Cables
12 amp Molex 1545 series connector
  In the past ARRL publications recommended
  Adequate for low power mobile radios, hand-helds, and accessories
  Can overheat and fail when used with high power equipment and heavy duty cycles
30 amp Anderson Powerpole connector
  Most groups now use
  Handle much greater current
  Capable of being plugged and unplugged many hundreds of times (operations) without deterioration

## Slide 41: Power Connectors and Cables

## Slide 42: Power Connectors and Cables (cont)
All power cables should be properly fused in both the positive and negative leads
  Fusing the negative leads helps to protect equipment from ground-fault currents
Vehicle "cigarette lighter plug" or "power point"
  May not able to deliver adequate current for mobile FM or HF radios operating at high power
  Direct connection to the vehicle battery
Know how much current your radio draws at different output power settings

## Slide 43: DC to AC Inverters
Not all inverters are suitable for use with radios, computers, or certain types of battery chargers
  Best inverters are those with a "true sine-wave"
  "modified sine-wave" output may not operate certain small battery chargers, and other waveform-sensitive equipment
  "high-frequency conversion" inverters generate significant RF noise if they are not filtered
Alternative to an inverter
  Mid-sized 12V computer UPS (uniterruptible power source)
    Smaller, square-wave UPS units are not designed for continuous duty applications
    Larger true sine-wave units are designed for continuous duty
Notes: Smaller, square-wave UPS units are not designed for continuous duty applications, but larger true sine-wave units are. Most true sine-wave units use internal batteries, but with minor modifications can be used with external batteries. The larger commercial UPS units run on 24 or 48 volts, and require two or four external batteries in series. UPS units will have a limit on the number of depleted batteries they can re-charge, but there is no limit to the number of batteries that can be attached to extend operating time.

## Slide 44: Equipment For Other Modes
Digital modes (packet, APRS, AMTOR, PSK31, etc)
  Computer and a TNC or computer sound card interface
  Software and cables
  Internal battery in your laptop computer
    External DC power supply and cable, or a DC to AC inverter
  Printer

## Slide 45: Packet

## Slide 46: Packet Radio Station

## Slide 47: Scanners and Other Useful Equipment
Multi-band scanning radio (to monitor public service and media channels)
FRS, GMRS or MURS hand-helds (more about these in LU 18)
Cellular telephone (even an unregistered phone can be used to call 911)
Portable digital recorder with VOX (for logging, recording important events)
AM/FM radio (to monitor media reports)
Portable television (to monitor media reports) once portable digital receivers are available
Weather Alert radio with "SAME" feature (to provide specific alerts without having to monitor the channel continuously)
Laptop computer with logging or emcomm-specific packet software
Sirius/XM Satellite Radio Receiver (Emergency Alert Channel)
Satellite television receiver (providers had “free” channel available during Katrina)

## Slide 48: Testing The Complete Station
After making your equipment selection (or beforehand if possible), field test it under simulated disaster conditions
  ARRL Field Day
Test all elements of your system together
  From power sources to antennas
  Try as many variations as possible

## Slide 49: Summary
Any questions before the quiz?

## Slide 50
Time for a Quiz
Take 30 Seconds adjust your workspace

## Slide 51
30
Seconds

## Slide 52
20
Seconds

## Slide 53
10
Seconds

## Slide 54
9
Seconds

## Slide 55
8
Seconds

## Slide 56
7
Seconds

## Slide 57
6
Seconds

## Slide 58
5
Seconds

## Slide 59
4
Seconds

## Slide 60
3
Seconds

## Slide 61
2
Seconds

## Slide 62
1
Seconds

## Slide 63
Let's get started!

## Slide 64: Topic 18 Question
In considering power sources for HF radios, which of the following is true?
  DC to AC inverters can be used to power HF radios
  Standard automotive batteries last longer than deep cycle batteries
  AC powered HF radios are suitable for all emcomm use
  Whenever possible, use deep cycle batteries to power HF radios

## Slide 65: Topic 18 Question
In considering antennas for VHF/UHF radios, which is the best rule?
  High transmitter power is more important than having a good antenna
  Transmitter power and antenna selection are equally important
  A good antenna is more important than high transmitter power
  If properly used, "rubber ducky" antennas can compensate for low transmitter power

## Slide 66: Topic 18 Question
Beam antennas have many advantages. Which of the following is the best reason for selecting a beam antenna?
  They are inexpensive and easy to transport
  They are easy to erect and very stable in storm conditions
  They are compact and easy to store
  They maximize desired signals and reduce interference from other stations

## Slide 67: Topic 18 Question
Which of the following statements about ARES deployment clothing is true?
  Three years (until 2013) are being given to “wear out” and replace older clothing
  The standards increase recognition and acceptance of ARES units
  The standards apply only to clothing worn on actual ARES deployments
  All of the above

## Slide 68: Topic 18 Question
In comparing the 30 amp Anderson power pole connector with the 10 amp Molex connector, which of the following statements is true?
  The Molex is better for high power applications
  The Molex is better for heavy duty cycles
  The Anderson handles only low power applications
  The Anderson is capable of being plugged and unplugged a greater number of times without deterioration

## Slide 69
B r e a k
10 Minutes

## Slide 70
10
Minutes

## Slide 71
5
Minutes

## Slide 72
2
Minutes

## Slide 73
1
Minute

## Slide 74
50
Seconds

## Slide 75
40
Seconds

## Slide 76
30
Seconds

## Slide 77
20
Seconds

## Slide 78
10
Seconds

## Slide 79
9
Seconds

## Slide 80
8
Seconds

## Slide 81
7
Seconds

## Slide 82
6
Seconds

## Slide 83
5
Seconds

## Slide 84
4
Seconds

## Slide 85
3
Seconds

## Slide 86
2
Seconds

## Slide 87
1
Seconds

## Slide 88
Let's get started!

## Slide 89: Any Questions Before Starting Topic 19?