## Slide 1: Training Volunteers
The ARRL
Introduction to Emergency Communication Course
EC-001 (2011)
Session Six
Notes: Make sure you have modified the Name and Date.
Display this screen as students are arriving for class.

## Slide 2: Reminder
Complete two DHS/FEMA Courses
    IS-100.b Introduction to ICS
    IS-700 National Incident Management System
      Http://training.fema.gov/IS/NIMS.asp
Notes: ARRL conditions!
The two ICS courses must be complete before taking the final exam.

## Slide 3: Session Five Topic
Session 1 – Topics 1, 2, 3, 4, 5a, 5b
Session 2 – Topics 6, 7a, 7b, 7c, 7d, 8, 9, 10
Session 3 – Topics 11, 12, 13, 14, 15
Session 4 – Topics 16, 17, 18, 19, 20
Session 5 – Topics 21, 22, 23, 24, 25, 26, 27
Session 6 – Topics 28, 29, Summary, Final Exam
Notes: The course requires a total of 18 hours.
If a student misses one class they can take a practice quiz for each lesson missed.
A student missing two sessions will be asked to take the course again.
A student missing the last session must wait for the next class and attend the final session for taking the exam again.
An exception would be two Field Examiners agreeing to give the exam at a mutually scheduled time.

## Slide 4: Topic 28 – Modes, Methods, and Applications

## Slide 5: Some Concepts to Consider
Communication modes fall into several categories:
  Point to point -- Telephone, fax, some digital radio modes
  Multi-point -- Voice and CW radio, some digital modes
  High precision -- Fax, e-mail, digital modes
  Low precision -- Voice, CW, telephone
  High priority -- Voice, telephone
  Low priority -- Fax, e-mail, digital modes, CW

## Slide 6: Some Concepts to Consider
Messages fall into similar categories:
  Point to point -- Messages intended for one party
  Point to multi-point -- Messages intended for a group
  Multi-point to point -- Messages from members of a group directed to one station
  High precision -- Lists of items, medical or technical terminology, specialized or detailed information
  Low precision -- Traffic reports, damage estimates, simple situation reports
  High priority -- Fast delivery is critical
  Low priority -- Messages can be delivered in a more relaxed time frame
Notes: Each type of message should be sent using the most appropriate mode, taking into consideration the message's contents, and its destination(s).

## Slide 7: Some Concepts to Consider
Each type of message should be sent using the most appropriate mode, taking into consideration the message's contents, and its destination(s)
Scenario
  A localized flash flood hit a north Florida county a few years ago, prompting the evacuation of a low-lying neighborhood. The Red Cross opened a shelter in a church several miles away from the affected area. ARES was mobilized to provide communication support.

## Slide 8: Example
The shelter still had electricity and phone service.
The ARES operator on duty was using his battery-operated 2-meter hand-held radio and the wide-area repeater to talk to Red Cross HQ across town.
The ham was reading a three-page list of names and addresses of evacuees who had checked into the shelter.
To ensure proper transcription, he was spelling each name phonetically, pausing after each name to see if the headquarters station needed fills.
  Time-consuming process. The operator had been reading for almost 15 minutes and was still on the second page of the list

## Slide 9: Example
Less than 10 feet away from his operating position sat a fax machine
The EC turned on the machine, dialed the Red Cross fax number, and fed in the remaining page of the list
The ham on duty had used over 15 minutes of air time and precious battery capacity to read two pages
The third page was faxed in less than 20 seconds

## Slide 10: Let’s do an After Action Report on Example
Training and practice had led them to concentrate on 2-meter voice to the exclusion of other modes of communication
So, instead of an efficient, point-to-point communication channel (telephone line), they had used a busy multi-point channel (the wide-area repeater)
Instead of using a mode that generated automatic hard copy, they used one that required handwritten transcription
Instead of a high-precision transfer (fax), they had used a low-precision one (voice) requiring spelling and phonetics
The repeater had been needed at the time for a different type of communication -- the transfer of mobile operator's reports
The "broadcast" of evacuee's names and addresses over non-secure communication channels was a violation of Red Cross policy

## Slide 11: Tactical Messages
Low-precision and time-critical
Can be passed most efficiently using voice
Can be formal written traffic
It may mean that the microphone is handed to a person from the served agency

## Slide 12: Lists and Detailed Messages
Long lists of supplies
Details where accuracy is important
Voice transmission can introduce errors
Long messages can waste valuable net resources
Digital modes (including land-line fax and email)
  Best means of handling these messages
  Fast and accurate
  “Repeatable accuracy”

## Slide 13: Sensitive Information
Names and addresses of evacuees should never be transmitted over voice channels
  Thieves with scanners can use this information to loot unattended homes
Digital transmissions require more than a simple scanner to intercept
  They cannot be relied upon for absolute privacy
If absolute privacy is required, the message should not be transmitted by Amateur Radio
  In some cases, the most appropriate method might be hand delivery by a radio-dispatched courier

## Slide 14: Digital Modes
Large volumes of written or high precision traffic
  Health and welfare traffic
  Logistics messages involving lists of people or supplies
Virtually error-free transmission
Relays can be accomplished by retransmitting the received digital message
Packet systems can provide automatic relays

## Slide 15: HF
Best digital modes for HF operation are
  Packet
  AMTOR mode B
  PSK31 in QPSK mode (error correction)

## Slide 16: VHF/UHF
TNC2 (Terminal Node Controller, Version 2) FM packet is the most common mode

## Slide 17: Packet
Error-free in point to point "automated repeat request" (ARQ) or "forward error correction"(FEC) broadcast modes
“Bulletin board"
  Sending station "posts" his messages on the bulletin board
  Other stations can then retrieve their messages at will
  Urgent messages can also be sent directly to the receiving station if needed

## Slide 18: Bulletin Boards
Useful when a number of stations are sending messages to a single point, such as a
  Command post,
  Weather service office, or
  Emergency operations center.
Useful in handling outgoing traffic.
  Stations with traffic can post messages to the bulletin-board
  Traffic handlers can periodically pick up the traffic and send it to the outbound NTS nets

## Slide 19: WiFi or 802.11
Used to link computers within a home or office
802.11b/g 2.4GHz wireless Ethernet
Amateurs have begun experimenting with long-range applications
July 2005 issue of QST
  Off-the-shelf consumer grade equipment
  Small dish antennas
  Paths up to 34 miles and data rates of 150KB

## Slide 20: AMTOR Mode B
AMateur Teleprinting Over Radio
  Sending station sends each character twice
  Receiving station does not acknowledge the data received
  If a receiving station matches both instances of a character, that character will be printed, otherwise some error symbol is printed
Advanced teletype mode
  With forward error correction
  Ideal for high precision messages over long distances

## Slide 21: PSK31
Phase Shift Keying, 31 Baud
  Keyboard-to-keyboard
Usable in very poor conditions makes it ideal for HF emergency communication
High efficiency
  Very narrow bandwidth
  Even a low power transmitter will work
BPSK, no error correction
QPSK, forward error-correction
BPSK should be used unless the received copy is poor, since QPSK is 3dB less efficient and requires more careful tuning.
Under all but the worst conditions, BPSK will provide perfect transmissions.

## Slide 22: Packet Teleprinting Over Radio (PACTOR)
Packet and AMTOR combination
HF use only
Uses FEC and ARQ modes
Standard keyboard
Quite robust
  Can be slowed by poor band conditions

## Slide 23: TCP/IP Packet
Advantages over conventional packet protocols
JNOS
  JNOS is a TCP/IP oriented e-mail system
  If you're familiar with Internet e-mail, you're familiar with typing e-mail into JNOS
  SMTP mail protocol and can interface to Internet
  Print incoming messages automatically onto a printer
  Up to eight windows for multiple sessions for messaging
  Supports multiple communications ports and multiple radio/TNC combinations
  Shareware
NOS (Network Operating System)

## Slide 24: APRS®
Automatic Position Reporting System
  Track a station's location
  GPS receiver
  Position information is transmitted to other stations using APRS packet software
  Displaying the location of the sending station on a map
  Messaging mode similar to Internet "Instant Messaging" where quick one-line messages can be exchanged
Automatic Packet Reporting System
  Automated reporting of data from digital weather stations

## Slide 25: APRS®
Emcomm APRS Use
  Locations of various emergency vehicles can be tracked visually in real time in an automated and unattended fashion
  Weather and other environmental data can be reported automatically in near real-time

## Slide 26: Winlink 2000
Digital email-to-radio network
  HF stations using Pactor
  VHF packet using local "TelPac" (telnet to packet) nodes

## Slide 27: D-Star
Digital email-to-radio network
  VHF/UHF
  Voice, text, packet
  Digital on 23 cm at 128 Kbps
  Callsign squelch

## Slide 28: Related Considerations
Become familiar with, and practice using, any digital mode or system well in advance of an emergency
  Most are complex enough that some experience is required to use them efficiently and effectively
High duty-cycle of many digital modes requires a rugged radio and power supply with adequate cooling

## Slide 29: Digital Equipment

## Slide 30: Amateur Television (ATV)
Slow-scan
  Uses a voice-grade channel to send a still picture line by line
  Can take more than a minute for a color picture to be transmitted
Fast-scan
  Live, full motion TV similar to what you see on commercial TV, but usually at reduced quality
No emcomm ATV transmission should ever be "staged" for the camera

## Slide 31: Amateur TV

## Slide 32: Summary
Any questions before the quiz?

## Slide 33
Time for a Quiz
Take 30 Seconds adjust your workspace

## Slide 34
30
Seconds

## Slide 35
20
Seconds

## Slide 36
10
Seconds

## Slide 37
9
Seconds

## Slide 38
8
Seconds

## Slide 39
7
Seconds

## Slide 40
6
Seconds

## Slide 41
5
Seconds

## Slide 42
4
Seconds

## Slide 43
3
Seconds

## Slide 44
2
Seconds

## Slide 45
1
Seconds

## Slide 46
Let's get started!

## Slide 47: Topic 28 Question
Which of the following describes your purpose as an emergency communicator?
  To operate the radio
  To coordinate communications for the EOC
  To provide accurate and rapid transfer of information from one place to another
  To provide internal communication support to one (and only one) responding agency

## Slide 48: Topic 28 Question
Which of the following best describes tactical messages?
  They are high precision and time critical
  They are low precision and time critical
  They are point-to-point and NOT time critical
  They are point-to-multipoint and low precision

## Slide 49: Topic 28 Question
Long lists and detailed messages are best handled by which of the following modes?
  Voice or CW
  Fax or digital
  CW or digital
  Phone or fax

## Slide 50: Topic 28 Question
During an emergency, you are using voice transmissions to pass messages. Which of the following "guidelines" should govern your action if you were asked to transmit the names and addresses of victims?
  Transmit the information exactly as presented to you
  Use a pre-established code to transmit the information
  If absolute privacy is required, do not transmit the information by Amateur Radio
  Switch to a digital mode and be assured of complete privacy

## Slide 51: Topic 28 Question
Which of the following PSK31 modes has an error correction feature?
  BPSK
  QPSK
  RPSK
  SPSK

## Slide 52: Any Questions Before Starting Topic 29?