## Slide 1: Training Volunteers
The ARRL
Introduction to Emergency Communication Course
EC-001 (2011)
Session Five
Notes: Make sure you have modified the Name and Date.
Display this screen as students are arriving for class.

## Slide 2: Reminder
Complete two DHS/FEMA Courses
    IS-100.b Introduction to ICS
    IS-700 National Incident Management System
      Http://training.fema.gov/IS/NIMS.asp
Notes: ARRL conditions!
The two ICS courses must be complete before taking the final exam.

## Slide 3: Session Five Topic
Session 1 – Topics 1, 2, 3, 4, 5a, 5b
Session 2 – Topics 6, 7a, 7b, 7c, 7d, 8, 9, 10
Session 3 – Topics 11, 12, 13, 14, 15
Session 4 – Topics 16, 17, 18, 19, 20
Session 5 – Topics 21, 22, 23, 24, 25, 26, 27
Session 6 – Topics 28, 29, Summary, Final Exam
Notes: The course requires a total of 18 hours.
If a student misses one class they can take a practice quiz for each lesson missed.
A student missing two sessions will be asked to take the course again.
A student missing the last session must wait for the next class and attend the final session for taking the exam again.
An exception would be two Field Examiners agreeing to give the exam at a mutually scheduled time.

## Slide 4: Topic 24 – Alternative Communication Methods

## Slide 5: Alternative Communications
Amateur radio may not always be the only or best radio service for the job
  There are dire situations in which individuals are forced to summon help by any means available
  Occasionally, we find that the tasks within a disaster exceed the limits of the manpower provided by the amateur community
  Sometimes it is better to hand an official a radio he can use to stay in contact with the ARES team on site, and not saddle him or her with a ham radio “shadow.”
    Particularly true for officials who must regularly deal with sensitive issues
  Other voluntary agencies may use these radio services in their own operations
Legal Considerations…

## Slide 6: Licenses
Some radio services require licenses, and others do not
  In a true emergency as defined by the FCC, this may not be a problem
FCC rules give everyone special permission to use "any means necessary" to communicate in order to protect life and property
  But only when no other normal means of communication is possible

## Slide 7: Licenses
If your group is planning to use licensed radios, obtain your license well before any emergency and keep it current
  If you own a radio, but no license, a judge could claim pre-meditation if you use it and disturb licensed users

## Slide 8: Can I Modify My Radio?
NO -- you cannot modify your radio and call for help on the local police frequency the next time you see a car crash on the highway
  Law enforcement agencies are not bound by the FCC’s rules.
Hams who have called for "help" on police frequencies have been convicted of "interfering with a police agency" under state and local laws, even though the FCC had taken no enforcement action.
Notes: In one case, the judge ruled that by modifying his radio in advance, the Amateur had committed "pre-meditated" interference, a serious charge. If you are in a position to save someone's life or property, be sure you are ready to defend your actions -- and possibly lose -- before pressing the mic button.

## Slide 9: Modified Amateur Radios
Easy to modify many VHF and UHF Amateur radios for operation in nearby public service and business bands
  Not legal to do so for regular "emergency" use
Radios must be "Type Accepted" by the FCC
  Amateur radios are not
Notes: If you plan to use other radio frequencies discussed in this unit, it is better to purchase the proper radio. However, if the need arises and your ham radio is all you have, the FCC will probably not prosecute you for using it - if the use falls within their strict rules for emergencies

## Slide 10: Citizens' Band (CB) Radio
No licensing is required, and tactical or self-assigned identifiers are acceptable
  A recommended method promoted by the FCC is the letter "K,” followed by the user's first and last initials, followed by your zip code
    “KBD98112”
  If you had a valid Class D License before the mid 1980s, you may continue to use your old CB call sign
DO NOT USE YOUR AMATEUR CALL SIGN

## Slide 11: CB Technical Information
11-meter band
40 designated channels from 26.965 to 27.405 MHz
Maximum output power of four watts
Amplitude modulation (AM)
Single side band (SSB)
FCC rules permit communication to a maximum of 250 km (155.3 miles)
Effective range averages between two and eight miles (mobile-mobile)
  Depending on antennas, terrain and propagation up to 25 miles (base-mobile)
SSB can significantly increase range
Channel 9 is reserved for emergency and motorist assistance traffic only
Notes: In many remote areas with little or no telephone service, families rely on CB radios for basic day-to-day communications. Many rural police and sheriff's organizations still monitor CB traffic. In a number of states, highway patrol officers install CB units in their patrol cars with the blessing of their agencies. However, may departments that used to monitor channel 9 have given up the practice. REACT groups in the area may still be monitoring.

## Slide 12: Multi-Use Radio Service (MURS)
Personal and business operation
Primarily intended for portable operation
Maximum power of two watts
MURS frequencies:
  151.820
  151.880
  151.940
  154.570
  154.600
Bandwidth on the first three frequencies is limited to 11.25 kHz, and 20 kHz for the last two
Frequency stability must be at least 5 ppm
Antenna height is limited to 60 feet above ground
No licenses are issued for this service

## Slide 13: Family Radio Service (FRS)
Designed for short-range personal communications
Good news
  Almost everyone owns one or more of these handy radios
Bad news
  Channels in some areas are crowded and undisciplined, making them less useful for emergency communications

## Slide 14: FRS Technical Information
14 available UHF channels
8 different CTCSS codes to limit background chatter and noise
Output power is from 100 to 500 mw
REACT recommends the use of FRS channel 1 (462.5625 MHz) with no CTCSS tone as an emergency calling channel
First 7 FRS channels are shared with the General Mobile Radio Service (GMRS)
  Chances of distress call being heard on either service is greatly increased on these seven common channels
Many FRS radio are offered as combination FRS/GMRS radios with up to two watts output on the GMRS channels
  License required
Notes: Unfortunately, the general public has not paid much attention to this "standard" and channel 1 is just as full of chatter as the others.
It is important to note that the channel numbers on each radio are not always interchangeable between older radios with fewer than 14 channels. The chart below shows the frequency relationships for many 2 and 14 channel radios. Single channel radios are usually on channel 1, which corresponds to channel 1 in the 14-channel units.

## Slide 15: General Mobile Radio Service (GMRS)
15 UHF frequencies between 462.5625 and 462.7250 MHz
  Eight are paired with matching repeater inputs five MHz higher
  7 “interstitial” channels are shared with FRS
  Power is limited to 50 watts
    Except on “interstitial” channels, 5 watts
There is no frequency coordination
  Users must cooperate locally to effectively use channels
CTCSS codes are the same as for FRS
FM voice operation is permitted
  Digital modes and phone patches are not
462.675 MHz is recognized for emergency and travel information use
  Monitored by many REACT teams nationwide

## Slide 16: GMRS
GMRS requires a license
Many “FRS” radios include “GMRS”
  You should have a license for these radios!
If you operate a radio under the rules that apply to GMRS, you must have a GMRS license.
GMRS radios generally transmit at higher power levels (1 to 5 watts is typical) and may have detachable antennas.
The current fee for a new GMRS license is $80.
The manual that comes
with the radio, or the label placed
on it by the manufacturer,
should indicate the service the
unit is certified for.
http://wireless.fcc.gov/services/index.htm?job=service_home&id=general_mobile
Notes: Operating a GMRS station will require a low-cost system license from the FCC. You can apply using FCC Form 574, or apply online. FCC online licensing information can be obtained at www.fcc.gov. System licenses are currently granted only to individuals. A system includes any and all radios operated by family members, and may include fixed, mobile, and repeater equipment. Use under the license is restricted to members of the licensee’s immediate family. Licenses to entities other than individuals are no longer issued, but non-individual entities licensed before July 31st, 1987 may continue to renew their licenses, and may not increase or modify their use.

## Slide 17: Public Safety Radio
There are instances where the use of police and fire radio frequencies is possible
  Agency itself might allow and train you for such use
  Individual officer may ask you to use his radio to call for help when he cannot
Keep your transmissions short and to the point
Do not tie up the channel with long explanations, and cease transmitting if they tell you to

## Slide 18: Cellular and PCS Phones
In a widespread disaster situation, these phone systems can quickly become overloaded
A message is too sensitive to send via any two-way radio, try your cell phone
  Cellular and PCS phone transmissions, especially digital, are considerably more secure
  In addition, it is possible to send low-speed data or fax transmissions over the cellular network

## Slide 19: Marine Radio
FM marine radios operate on internationally allocated channels in the 160 MHz band
HF SSB radios operate on a variety of ITU channels between 2 and 30 MHz
FM stations for vessels in US waters do not require a license
Operation on the HF channels does require a license
Channel 16 – Distress Channel
  If you hear a vessel in distress whose calls are going unanswered by the Coast Guard, you may legally answer them from an unlicensed land-based station under the FCC’s “emergency communications” rules

## Slide 20: Aviation Radio
AM radios operating in the 108-136 MHz band
  FCC licenses are required for all aircraft stations operating internationally, but not within the US
Emergency locator transmitters (ELTs)
  Automatic devices that transmit a distress signal on 121.5 (civilian distress channel) and 243.0 MHz (military counterpart)
  Also used for marine Emergency Position Indicating Radio Beacons (EPIRB) and the new land-based Personal Radio Beacons (PRB)

## Slide 21: Non-Radio Communications
If they are still functioning, use the telephone and fax whenever the message might be too sensitive for radio
Fax is also useful for sending long lists, and where accuracy is critical
Do not tie up a radio frequency sending a long list of supplies if a working fax or phone is available

## Slide 22: Couriers
Sensitive or very lengthy message
  Fax and phone lines are out of service
Hand delivery might be the best choice if travel is possible
Acting as a courier does not
eliminate the use of radio,
since couriers need to be
dispatched from place to place

## Slide 23: And Don’t Forget
Internet
Email
WebEOC
Packet

## Slide 24: Summary
Any questions before the quiz?

## Slide 25
Time for a Quiz
Take 30 Seconds adjust your workspace

## Slide 26
30
Seconds

## Slide 27
20
Seconds

## Slide 28
10
Seconds

## Slide 29
9
Seconds

## Slide 30
8
Seconds

## Slide 31
7
Seconds

## Slide 32
6
Seconds

## Slide 33
5
Seconds

## Slide 34
4
Seconds

## Slide 35
3
Seconds

## Slide 36
2
Seconds

## Slide 37
1
Seconds

## Slide 38
Let's get started!

## Slide 39: Topic 24 Question
Which can you NOT use to identify your transmissions on Citizens' Band radio?
  Your Amateur call
  Your “handle”
  A self-assigned identifier
  A tactical call sign

## Slide 40: Topic 24 Question
Which is the best course of action for summoning help via CB?
  Use channel 1, since the lowest frequency has the longest ground-wave signal
  Call at regular intervals on Channels 9 and 19 for a response
  Call only on channel 9, since it is designated for assistance and emergencies
  Say "Break-Break" or "MAYDAY" on any channel

## Slide 41: Topic 24 Question
Which is NOT an advantage of using Family Radio Service (FRS) systems?
  They are readily available at low cost
  Operation of FRS radios is simple and requires little training
  There is no requirement for licensing to use FRS
  Low transmitter power

## Slide 42: Topic 24 Question
Who may currently license a GMRS system with the FCC?
  A privately owned business, for routine communications
  An individual, for family and personal use
  A charitable institution, for benevolent purposes
  A local repeater club

## Slide 43: Topic 24 Question
Which is NOT true of the MURS?
  A station license is required
  Power output is limited to 2 watts
  Radios operate in the VHF band
  Data emissions are permitted

## Slide 44
B r e a k
10 Minutes

## Slide 45
10
Minutes

## Slide 46
5
Minutes

## Slide 47
2
Minutes

## Slide 48
1
Minute

## Slide 49
50
Seconds

## Slide 50
40
Seconds

## Slide 51
30
Seconds

## Slide 52
20
Seconds

## Slide 53
10
Seconds

## Slide 54
9
Seconds

## Slide 55
8
Seconds

## Slide 56
7
Seconds

## Slide 57
6
Seconds

## Slide 58
5
Seconds

## Slide 59
4
Seconds

## Slide 60
3
Seconds

## Slide 61
2
Seconds

## Slide 62
1
Seconds

## Slide 63
Let's get started!

## Slide 64: Any Questions Before Starting Topic 25?