## Slide 1: Training Volunteers
The ARRL
Introduction to Emergency Communication Course
EC-001 (2011)
Session Two
Notes: Make sure you have modified the Name and Date.
Display this screen as students are arriving for class.

## Slide 2: Reminder
Complete two DHS/FEMA Courses
    IS-100.b Introduction to ICS
    IS-700 National Incident Management System
      Http://training.fema.gov/IS/NIMS.asp
Notes: ARRL conditions!
The two ICS courses must be complete before taking the final exam.

## Slide 3: Session Two Topic
Session 1 – Topics 1, 2, 3, 4, 5a, 5b
Session 2 – Topics 6, 7a, 7b, 7c, 7d, 8, 9, 10
Session 3 – Topics 11, 12, 13, 14, 15
Session 4 – Topics 16, 17, 18, 19, 20
Session 5 – Topics 21, 22, 23, 24, 25, 26, 27
Session 6 – Topics 28, 29, Summary, Final Exam
Notes: The course requires a total of 18 hours.
If a student misses one class they can take a practice quiz for each lesson missed.
A student missing two sessions will be asked to take the course again.
A student missing the last session must wait for the next class and attend the final session for taking the exam again.
An exception would be two Field Examiners agreeing to give the exam at a mutually scheduled time.

## Slide 4: Topic 7c - Net Operating Guidelines

## Slide 5: The Net Manager
Responsible for:
  Recruiting and training NCS operators, liaison stations, and other net members
  Sets up the net's schedule
  Makes sure qualified NCS operators are available
  Arrange for relief operators and support services
May be responsible for more than one net

## Slide 6: The NCS
"ringmaster" or "traffic cop"
Decides what happens in the net, and when
Decides when stations will check in, with or without traffic, and whether messages will be passed on the net's frequency or a different one
Needs to be aware of everything going on around him and handle the needs of the net, its members, and served agency as quickly and efficiently as possible

## Slide 7: The NCS
NCS can be located anywhere, but should be in a position to hear most, if not all, stations in the net
  At EOC or command post,
The NCS should not be responsible for the entire emcomm operation
Notes: It is not possible to be in command of all aspects of an emergency response, and still run a net effectively, since both jobs require 100% of your attention

## Slide 8: Net Scripts
Many groups open and close their nets with a standard script
  Lets listeners know the purpose and format of the net
  Ensures that the net will be run in a similar format regardless of who is NCS

## Slide 9: Net Scripts – Basic Components
Identify the NCS and Net purpose
Check in procedures
Priority traffic
Check-ins
{…………}
Closing

## Slide 10: The Backup NCS
Readily available if:
  An equipment failure at the primary NCS location
  The primary NCS operator needs to take a break
Two types:
  At the same location as the primary NCS
  At a different location
    Maintains a duplicate log of everything happening during the net

## Slide 11: Acting as a "fill-in" NCS
Basic dos and don'ts
  Remember that although you are in control of the net, you are not "God." Treat members with respect and accept suggestions from other experienced members.
  If you are taking over an existing net, try to run it much as the previous NCS did.
  Always follow a script if one is provided. Write your own if necessary, but keep it short and to the point.
  Handle messages in order of precedence: Emergency Priority Welfare.

## Slide 12: Acting as a "fill-in" NCS
More Basic dos and don'ts
  Speak clearly and in a normal tone of voice. Use good mic technique.
  Make all instructions clear and concise, using as few words as possible.
  Keep notes as you go along. Do not let your log fall behind.
  Write down which operators are at which locations. When one leaves or is replaced, update your notes.
  Ask stations to pass messages off the main net frequency whenever possible.
All the reading and study in the world
will not replace actual experience

## Slide 13: Net Members
Operators at various sites are responsible for messages going to and from their location
  Listen to everything that happens on the net
  Maintain contact with the served agency
Assist the served agency with the creation of messages, put them into the appropriate format, and contact the NCS when they are ready to be sent
Ideally, two operators should be at each site
Notes: When the station is busy, one can handle logging, message origination, and work with the served agency's staff while the other monitors the net, sends messages, and copies incoming traffic. During slower periods, one member can be "off-duty" for rest, meals, or personal needs.

## Slide 14: Bulletin Stations
Relays ARRL bulletins or those authorized by the served agency to all stations in the net
  May be transmitted on a preset schedule, such as at the top and bottom of each hour.
Must be located at the served agency
  Or have a reliable communication link to them

## Slide 15: Liaison Stations
Pass messages between two different nets
  As needed, or on a pre-set schedule
Liaison station may monitor one net full time
  When a message must be passed to another net, they leave the net temporarily to pass it, and then return
  The other net has a liaison station who does exactly the same thing, but in reverse

## Slide 16: Liaison Stations
Single liaison station may need to handle messages going both ways between two nets
  Use two radios to monitor both nets at the same time
    Difficult if either or both nets are busy
  One radio is used
    Switch between the two nets on a regular schedule

## Slide 17: Relay Stations
Passes messages between two stations in the net that cannot hear each other
  Not a regular net position
  On an "as needed" basis
If you can hear a station or stations that the NCS cannot, it is OK to volunteer to act as a relay station

## Slide 18: Workload and Shifts
No operator should try to work excessively long hours
efficiency and effectiveness decline
served agency is not getting the best possible service
Ensure that all net members get some rest on a regular basis

## Slide 19: Shift Changes
Monitor the net for at least fifteen minutes
Review the logs with the present operator before taking over
  Continuity in the net's operation

## Slide 20: Non-Voice Modes
Packet
  FM packet, HF packet, and PACTOR
  No real “packet net”
    Provide an automatic connection between two stations
    Transmit "traffic" using the bulletin board or mailbox facility of the TNC
  Automatically routed and stored without any action by the receiving station's operator or a NCS

## Slide 21: Non-Voice Modes
Non-packet digital modes
  RTTY, PSK31, AMTOR, and GTOR
  Not automatic
  May require a NCS operator to manage the net

## Slide 22: Non-Voice Modes
CW Procedures
  Clean and accurate code sent at 10 words per minute is better than sloppy code sent at 30 words per minute
  Send at the receiving speed
  ARRL FSD-218 “Pink Card”
  Be consistent with abbreviations and prosigns

## Slide 23: Interference Problems
Adjacent or co-channel stations who may be unaware of the emergency net
  Politely inform them of the net and ask for their cooperation
    Ask an HF net to move over a few kHz
If the problem cannot be resolved
  Have one or more alternative frequencies
Never discuss, acknowledge, or try to speak with
an intentionally interfering station
Notes: Many years of experience has proven that this only encourages the offender. If the interference is making communication difficult, simply announce to the net that everyone should move to the alternate frequency and sign off. Better yet, put a plan in place so that when interference occurs, all net members know to move to the alternate frequency without being told to do so on the air.
If the intentional interference persists, the Net Manager or NCS can contact an elected League official or an Official Observer Station, and ask that the FCC be notified of the interference. In some cases they may be able to track down and contact the responsible station.

## Slide 24: L.A. Area Radio Jammer Convicted
September 2006, L.A. resident Jack Gerritsen (ex-KG6IRO), now 70, convicted of willful and malicious interference and transmitting without a license
  Repeat offender  15 prior misdemeanor convictions
  Conducted on-air tirades and outright jamming
  Performed willful and malicious interference to communications system operated by the US Coast Guard Auxiliary during a 2004 search-and-rescue operation
  Interfered with American Red Cross radio transmissions in early 2005 while the agency was preparing for disaster relief operations
  Caused cancellation of a US Army Reserve homeland security training exercise in 2005 by interfering with US Army Military Affiliate Radio System (MARS) communications
Punishment
  Amateur Radio license & call sign revoked
  Radio equipment confiscated
  Can not use any moniker for identification (e.g. call sign)
  Prohibited from owning, possessing or using any radio equipment
  Fined $15,225
  Sentenced to seven years in federal prison
Extreme case and fortunately a rarity

## Slide 25: Summary
Any questions before the quiz?

## Slide 26
Time for a Quiz
Take 30 Seconds adjust your workspace

## Slide 27
30
Seconds

## Slide 28
20
Seconds

## Slide 29
10
Seconds

## Slide 30
9
Seconds

## Slide 31
8
Seconds

## Slide 32
7
Seconds

## Slide 33
6
Seconds

## Slide 34
5
Seconds

## Slide 35
4
Seconds

## Slide 36
3
Seconds

## Slide 37
2
Seconds

## Slide 38
1
Seconds

## Slide 39
Let's get started!

## Slide 40: Topic 7c Question
Which of the following best describes the responsibilities of the NCS in an emcomm operation?
  The NCS is responsible for all aspects of the emcomm operation
  The NCS is responsible for station check in
  The NCS is responsible for all aspects of the net's operation
  The NCS is responsible for writing the net script

## Slide 41: Topic 7c Question
As acting "fill in" NCS, which of the following practices would you avoid?
  Try to run an existing net much as the previous NCS did
  Handle messages in order of precedence: Emergency-Priority-Welfare
  Keep notes as you go along: do not let your log fall behind
  Ask stations to pass messages on the main net frequency whenever possible

## Slide 42: Topic 7c Question
Which of the following is true of a liaison station?
  The liaison station mainly relays bulletins authorized by the served agency to all stations on the net
  A liaison station passes messages only on a pre-set schedule
  A liaison station handles only one-way traffic
  A liaison station passes messages between two nets

## Slide 43: Topic 7c Question
Packet modes include which of the following groups?
  FM packet, HF packet and PACTOR
  HF packet, PACTOR and PSK31
  PACTOR, PSK31 and RTTY
  PSK31, RTTY and PACTOR

## Slide 44: Topic 7c Question
You are the NCS of a net involved in an emcomm operation and you notice that some other station is intentionally interfering with your net. Which of the following represents your best course of action?
  Shut down the net and go home
  Address the interfering station directly and inform them of the error of their ways
  Move the net to an alternate frequency
  Contact the EOC and continue to operate

## Slide 45: Any Questions Before Starting Topic 7d?