## Slide 1: Training Volunteers
The ARRL
Introduction to Emergency Communication Course
EC-001 (2011)
Session Five
Notes: Make sure you have modified the Name and Date.
Display this screen as students are arriving for class.

## Slide 2: Reminder
Complete two DHS/FEMA Courses
    IS-100.b Introduction to ICS
    IS-700 National Incident Management System
      Http://training.fema.gov/IS/NIMS.asp
Notes: ARRL conditions!
The two ICS courses must be complete before taking the final exam.

## Slide 3: Session Five Topic
Session 1 – Topics 1, 2, 3, 4, 5a, 5b
Session 2 – Topics 6, 7a, 7b, 7c, 7d, 8, 9, 10
Session 3 – Topics 11, 12, 13, 14, 15
Session 4 – Topics 16, 17, 18, 19, 20
Session 5 – Topics 21, 22, 23, 24, 25, 26, 27
Session 6 – Topics 28, 29, Summary, Final Exam
Notes: The course requires a total of 18 hours.
If a student misses one class they can take a practice quiz for each lesson missed.
A student missing two sessions will be asked to take the course again.
A student missing the last session must wait for the next class and attend the final session for taking the exam again.
An exception would be two Field Examiners agreeing to give the exam at a mutually scheduled time.

## Slide 4: Topic 27 – Marine Communications

## Slide 5: Definitions
Vessel: A general term for all craft capable of floating on water and larger than a rowboat.
Ship: A general term for larger seagoing vessels of every kind.
Boat: A term applied to smaller craft propelled by oars, sails or engines.
Marine: An adjective meaning related to or connected with the sea.

## Slide 6: Marine Radio
VHF-FM, (156 to 162 MHz)
  Effective range from ship to ship of 10 to 15 miles, and ship to shore of 20-30 miles
Vessels that routinely travel outside this distance generally have MW/HF-SSB, satellite communications or both
CW communication on MW/HF is no longer used
No license is currently required for pleasure boats operating on the FM channels in US territorial waters

## Slide 7: VHF-FM
FCC limits VHF-FM marine radios to a maximum of 25 watts
  Radios are also required to be capable of 1-watt operation for short range and in-harbor use
VHF and MW/HF marine radio use is restricted to vessels on the water
  The use of portables or mobiles to communicate with crew on shore is not allowed
  Marinas, marine towing services, and fish canneries may be licensed for limited base operations on certain channels
Notes: In an emergency, however, the FCC rules are suspended, and you may use whatever means of communication are necessary to protect life and property.

## Slide 8: Channel Selection
Marine FM frequencies have been assigned channel numbers
  Channel 16 has been designated worldwide as a distress and calling frequency
  All vessels are required to maintain a listening "watch" on FM 16 while underway
  FM 9 has been designated as an alternate calling frequency

## Slide 9: Frequencies for key marine VHF channels
FM 9 | 156.45 | Calling | FM 22 | 157.1 | Coast Guard - NOTAMS
FM 16 | 156.8 | Calling/Distress | FM 23 | 157.15 | Coast Guard
FM 17 | 156.85 | State/local gov't shore sta. | FM 68 | 156.425 | Intership
FM 18 | 156.9 | Commercial Intership | FM 69 | 156.475 | Intership
FM 21 | 157.05 | Coast Guard | FM 83 | 157.175 | Coast Guard Auxillary

## Slide 10: Restricted Channels
Some channels are not for public use
FM 83 is reserved for use by the Coast Guard Auxiliary
FM 22 is for public communication with the Coast Guard, but may not be used by boaters unless specifically instructed to do so by the Coast Guard radio operator on FM 16
FM 22 is also used by the Coast Guard to broadcast "Notice To Mariners" messages (NOTAMS), after announcing them on FM 16.
FM 6 is an Inter-Ship Safety channel, and is often used for search and rescue operations.
List of all marine channels and their assigned uses can be seen at www.fcc.gov/wtb/marine/vhfchanl.html.

## Slide 11: Spoken Emergency Signals
"MAYDAY MAYDAY" — The highest priority urgency call.
  Vessel calling is threatened by grave or immediate danger and requires immediate assistance
"PAN PAN" (pronounced "pawn-pawn") — known as an "urgency" call
  Vessel calling has an urgent message concerning the safety of a vessel or person
"SECURITE" (pronounced "securitay")
  Official messages about the safety of navigation or important weather warnings
"SILENCE"
  Declared by Coast Guard
  Only units involved in incident may transmit on frequency under order lifted by Coast Guard

## Slide 12: Incident Reporting
Two types of incidents that hams may need to report directly to the Coast Guard
  Vessels in distress
    Reported directly to the nearest Coast Guard station
  Oil or chemical spills into public waters
    Coast Guard's National Response Center at 1-800-424-8802
    NRC Internet Web site www.nrc.uscg.mil

## Slide 13: Distress Calls
Listen first to see if the Coast Guard responds within a minute or two
If not, attempt to gather the following information:
  Position of the vessel involved
  Number of persons on board
  Nature of the distress
  Name of the vessel
  Call sign (if any)
  Length and type of vessel
  Color
  Any descriptive features — number of masts, flying bridge, etc
  Weather conditions on scene
  On board emergency equipment: life raft, Emergency Position Indicating Radio Beacon (EPIRB) and class of EPIRB if possible
  Frequency being used to communicate with the vessel
Notes: Once you have the information, advise all persons on board to don life jackets, and contact either 911 dispatch or the closest Coast Guard facility by phone. In some cases, a local fire or police boat may be able to respond more quickly than the Coast Guard, who may be some distance away. Identify yourself as an Amateur Radio operator relaying an emergency message. Pass on all the information that you have gathered and assist as requested. Provide your name and phone number or other means of contact so that responding local public safety agencies or the Coast Guard may reach you if needed. It is possible that you are the only station that can communicate with the distressed vessel.

## Slide 14: Distress Calls
Contact either 911 dispatch or the closest Coast Guard facility by phone
  In some cases, a local fire or police boat may be able to respond more quickly than the Coast Guard
Identify yourself as an Amateur Radio operator relaying an emergency message
Pass on all the information that you have gathered and assist as requested
Provide your name and phone number or other means of contact so that responding local public safety agencies or the Coast Guard may reach you if needed

## Slide 15: Routine Communication
Calling a vessel on a marine channel is very similar to 2 meters
If using channel 9, transmit the name of the vessel you want to talk with twice, followed by your station’s name twice, and the channel designation.
  "Fishy Business, Fishy Business, this is Dream Boat, Dream Boat, Channel 9“
Listen for at least 30 seconds before repeating the call
Once you get an answer, direct the station to shift to a "working" channel
  "Fishy Business this is Dream Boat; shift to channel 69"

## Slide 16: Routine Communication
FCC rules require you to identify your vessel on each transmission, although some stations shift to a shortened call after the initial contact is established
The use of 10 codes and "Q" signals is not permitted on marine VHF-FM

## Slide 17: MW/HF SSB Communications
U.S Coast Guard maintains "guard" on 2182 kHz
  Calling and distress frequency
MW and HF maritime frequencies and assignments
  www.navcen.uscg.gov/marcomms/high_frequency/default.htm
Many boaters carry HF amateur radio aboard.
  Amateur Radio Maritime Nets
  www.arrl.org/FandES/field/nets/

## Slide 18: Summary
Any questions before the quiz?

## Slide 19
Time for a Quiz
Take 30 Seconds adjust your workspace

## Slide 20
30
Seconds

## Slide 21
20
Seconds

## Slide 22
10
Seconds

## Slide 23
9
Seconds

## Slide 24
8
Seconds

## Slide 25
7
Seconds

## Slide 26
6
Seconds

## Slide 27
5
Seconds

## Slide 28
4
Seconds

## Slide 29
3
Seconds

## Slide 30
2
Seconds

## Slide 31
1
Seconds

## Slide 32
Let's get started!

## Slide 33: Topic 27 Question
When is it permissible to utilize channel FM 22?
  At anytime after making an initial call on FM 16
  Whenever channel FM 9 or FM 16 are busy
  Only when directed by the Coast Guard
  At no time; it is for Coast Guard use only

## Slide 34: Topic 27 Question
What should you do if you hear an unanswered marine distress call?
  Contact the nearest Coast Guard facility and advise them of the call
  Answer the caller immediately and ask what the emergency is
  Get in your own boat and attempt a rescue
  Listen for a response. If none, respond and gather all information possible and then contact the nearest Coast Guard facility

## Slide 35: Topic 27 Question
When must you identify yourself on VHF-FM marine radio?
  Only on the initial call
  Only on the initial call and the final call
  Only on the original call and then every ten minutes
  On all transmissions

## Slide 36: Topic 27 Question
Which vessels operate MW/HF SSB radios?
  Any vessel that wants to
  Only sea-going vessels that operate outside the range of VHF-FM radios
  Only those vessels that operate offshore and have a VHF-FM marine radio
  Only those vessels that have an Amateur Radio operator aboard

## Slide 37: Topic 27 Question
Which channel(s) may be used for calling another vessel?
  FM 83
  FM 9
  FM 16
  Both FM 9 and FM 16

## Slide 38: Any Questions Before Ending This Session?
End Session