## Slide 1: Training Volunteers
The ARRL
Introduction to Emergency Communication Course
EC-001 (2011)
Session Three
Notes: Make sure you have modified the Name and Date.
Display this screen as students are arriving for class.

## Slide 2: Reminder
Complete two DHS/FEMA Courses
    IS-100.b Introduction to ICS
    IS-700 National Incident Management System
      Http://training.fema.gov/IS/NIMS.asp
Notes: ARRL conditions!
The two ICS courses must be complete before taking the final exam.

## Slide 3: Session Three Topic
Session 1 – Topics 1, 2, 3, 4, 5a, 5b
Session 2 – Topics 6, 7a, 7b, 7c, 7d, 8, 9, 10
Session 3 – Topics 11, 12, 13, 14, 15
Session 4 – Topics 16, 17, 18, 19, 20
Session 5 – Topics 21, 22, 23, 24, 25, 26, 27
Session 6 – Topics 28, 29, Summary, Final Exam
Notes: The course requires a total of 18 hours.
If a student misses one class they can take a practice quiz for each lesson missed.
A student missing two sessions will be asked to take the course again.
A student missing the last session must wait for the next class and attend the final session for taking the exam again.
An exception would be two Field Examiners agreeing to give the exam at a mutually scheduled time.

## Slide 4: Topic 13 – Severe Weather Nets

## Slide 5: SKYWARN®
Registered name
National Weather Service (NWS)
A program like “ARES” is
ARRL MOU
“Ground Truth” observations are invaluable
First response group
Certificate for training

## Slide 6: What is reported?
Specific Critical Weather Observations
Amateurs without SKYWARN® training
Check-in with SKYWARN® spotter number
Out of the ordinary weather events

## Slide 7: What is reported? (cont)
Four step method
What: Tornadoes, funnel clouds, heavy rain, etc.
Where: Direction, distance; “3 miles south of Newington Center on Route 15”
When: Time of observation
Details: {…fill in the blanks…}

## Slide 8: Activation
Observers should be monitoring
NOAA All Hazards Weather Radio 162.400
The SKYWARN® net may be formally activated upon request of the NWS or net members

## Slide 9: Operating the Weather Net
Based on local needs
NCS where necessary
ARES may designate an EC or AEC liaison
NWS may have an Amateur Station
HT may be provided
Treat as formal traffic after net activation

## Slide 10: The Hurricane Watch Net (HWN)
Eyes and ears for NWS
National Hurricane Center – WX4HNC
Two differences from SKYWARN®
  Volunteers are exclusive Amateur Radio Operators
  Primarily on HF-SSB
Membership is not restricted
Activates when a hurricane is a threat to land (~300 miles)
Limited check-ins

## Slide 11: Primary Functions of HWN
Disseminate advisory information
Obtain ground-level weather observations
Function as a backup wide-area communications link
Relay initial assessments of hurricane damage

## Slide 12: Safety Concerns for All Weather Net Stations
Protect yourself first
Evacuate when asked
Protect antennas from high winds and power lines
Locate away from flooded/flooding areas

## Slide 13: VoIP Modes
Echolink
IRLP and Echolink have upward of 100 connections; repeaters and conference rooms
VoIP-WX Net for those without HF
HWN operates on 14.325 MHz

## Slide 14: Weather Net Operating Tips
More than one time zone – use UTC time
Give details accurately and completely
Watch out for sensitive information
Use PTT not VOX
Guard against background noise

## Slide 15: Summary
Any questions before the quiz?

## Slide 16
Time for a Quiz
Take 30 Seconds adjust your workspace

## Slide 17
30
Seconds

## Slide 18
20
Seconds

## Slide 19
10
Seconds

## Slide 20
9
Seconds

## Slide 21
8
Seconds

## Slide 22
7
Seconds

## Slide 23
6
Seconds

## Slide 24
5
Seconds

## Slide 25
4
Seconds

## Slide 26
3
Seconds

## Slide 27
2
Seconds

## Slide 28
1
Seconds

## Slide 29
Let's get started!

## Slide 30: Topic 13 Question
When is the Hurricane Watch Net normally activated?
  Every morning at 1000 UTC during hurricane season only
  When a hurricane is within 300 miles of making landfall
  When a tropical storm approaches a populated land mass
  When a tropical wave develops west of Africa

## Slide 31: Topic 13 Question
Who should check in to the Hurricane Watch Net an hour before a hurricane makes landfall?
  All amateurs should check in
  Amateurs with weather stations only
  Only those stations on the net roster
  Only amateurs in the affected area, or amateurs with important information that would be needed by the net or the National Hurricane Center

## Slide 32: Topic 13 Question
Does a station have to be located in a hurricane area to be a member of the Hurricane Watch Net?
  Yes, the net is made up solely of stations in hurricane areas
  There is no membership in the Hurricane Watch Net. Anybody can check in at any time.
  No. The net has a need for stations in Canada and on the west coast that can control the net as propagation shifts to the north and to the west
  No. The net has a need for stations in the Midwest and west coast that can control the net as propagation shifts to the west

## Slide 33: Topic 13 Question
Which answer best describes the four step method to describe severe weather?
  Who, What, When, Why
  What, Where, When, Details
  What, Where, Why, General Comments
  What, When, Why, Where

## Slide 34: Topic 13 Question
SKYWARN® participants would generally not report which of the following?
  Fog
  High winds
  Sleet
  Hail size

## Slide 35
B r e a k
10 Minutes

## Slide 36
10
Minutes

## Slide 37
5
Minutes

## Slide 38
2
Minutes

## Slide 39
1
Minute

## Slide 40
50
Seconds

## Slide 41
40
Seconds

## Slide 42
30
Seconds

## Slide 43
20
Seconds

## Slide 44
10
Seconds

## Slide 45
9
Seconds

## Slide 46
8
Seconds

## Slide 47
7
Seconds

## Slide 48
6
Seconds

## Slide 49
5
Seconds

## Slide 50
4
Seconds

## Slide 51
3
Seconds

## Slide 52
2
Seconds

## Slide 53
1
Seconds

## Slide 54
Let's get started!

## Slide 55: Any Questions Before Starting Topic 14?