## Slide 1: Training Volunteers
The ARRL
Introduction to Emergency Communication Course
EC-001 (2011)
Session Two
Notes: Make sure you have modified the Name and Date.
Display this screen as students are arriving for class.

## Slide 2: Reminder
Complete two DHS/FEMA Courses
    IS-100.b Introduction to ICS
    IS-700 National Incident Management System
      Http://training.fema.gov/IS/NIMS.asp
Notes: ARRL conditions!
The two ICS courses must be complete before taking the final exam.

## Slide 3: Session Two Topic
Session 1 – Topics 1, 2, 3, 4, 5a, 5b
Session 2 – Topics 6, 7a, 7b, 7c, 7d, 8, 9, 10
Session 3 – Topics 11, 12, 13, 14, 15
Session 4 – Topics 16, 17, 18, 19, 20
Session 5 – Topics 21, 22, 23, 24, 25, 26, 27
Session 6 – Topics 28, 29, Summary, Final Exam
Notes: The course requires a total of 18 hours.
If a student misses one class they can take a practice quiz for each lesson missed.
A student missing two sessions will be asked to take the course again.
A student missing the last session must wait for the next class and attend the final session for taking the exam again.
An exception would be two Field Examiners agreeing to give the exam at a mutually scheduled time.

## Slide 4: Topic 9 – The Net Control Station (NCS) Operator Practices

## Slide 5: Before Opening a Net
All stations heard from this location?
Is there minimal disruption in this location?
Is this the best antenna?
Is there battery backup?
Headset – with noise canceling microphone

## Slide 6: Before Opening a Net (cont)
Office supplies to last the shift
Familiar with VHF/UHF repeater(s)
Liaisons and loggers
Backup NCS
Relief operator

## Slide 7: Open/Close a Net
Scheduled Nets
  Training
Emergency Nets
  When Needed
It is best to use a script to open or close the net
This is W1HQ calling the Elmer Fudd County Emergency Net. This is a directed net, and all stations must call Net Control only. This net is handling only Emergency and Priority Traffic at this time. Only ARES stations assigned to this net should participate. Once checked in, please check out with Net Control before leaving the frequency. Stations with emergency traffic may check in now, or break the net at any time.

## Slide 8: Message Precedence
Emergency
Priority
Health & Welfare
Routine
The primary job of the NCS operator is to ensure that the messages with the highest precedence are sent first!

## Slide 9: Asking for Check-Ins
Immediately after the opening script and periodically
State often what type messages are being handled
Check-ins with traffic first by priority
Ask for check-ins at least every 15 minutes
Verify check-ins by repeating the callsign
  Reduces time required for checkins
Studies show that “This is” and unkeying before sending callsign just waste time.
When in doubt - Follow local procedures

## Slide 10: Time Tested Techniques
Listen Carefully
Check-ins – acknowledge- fills
Pair up traffic on a different frequency
Explain your style if necessary
Be concise
Frequent breaks
Tone of voice
ID often (FCC)
Notes: It is not possible to be in command of all aspects of an emergency response, and still run a net effectively, since both jobs require 100% of your attention

## Slide 11: Net Disciplines
Trained net members will:
  Report as soon as assigned
  Ask permission to call another station
  Answer promptly when called
  Use tactical callsigns
  ID (FCC) at the end of each exchange
  Follow protocol
Remember these are volunteers!

## Slide 12: Microphone Technique
Articulate – don’t slur
Slow down – stop the rapid fire
Select the best microphone
  Noise-canceling
  Unidirectional
  Omnidirectional
  Hisses and pops

## Slide 13: More Hints for Successful Operation
Use only plain English and standard prowords
Short transmissions
Scheduled nets should start on time
Be friendly
Ask for assistance
Mistakes will be made
Transmit only facts
Use standard ITU phonetics

## Slide 14: Summary
Any questions before the quiz?

## Slide 15
Time for a Quiz
Take 30 Seconds adjust your workspace

## Slide 16
30
Seconds

## Slide 17
20
Seconds

## Slide 18
10
Seconds

## Slide 19
9
Seconds

## Slide 20
8
Seconds

## Slide 21
7
Seconds

## Slide 22
6
Seconds

## Slide 23
5
Seconds

## Slide 24
4
Seconds

## Slide 25
3
Seconds

## Slide 26
2
Seconds

## Slide 27
1
Seconds

## Slide 28
Let's get started!

## Slide 29: Topic 9 Question
Which of the following statements is true?
  The NCS should ask for check-ins immediately before reading the opening script
  The NCS should ask for check-ins just before reading the closing script
  The NCS should ask for check-ins immediately after reading the opening script and periodically thereafter
  The NCS should ask for check-ins every ten minutes during the operation of the net

## Slide 30: Topic 9 Question
In which order should messages be handled during an emergency?
  Priority, Emergency, Health & Welfare, Routine
  Emergency, Priority, Health & Welfare, Routine
  Emergency, Health & Welfare, Priority, Routine
  Health & Welfare, Emergency, Routine, Priority

## Slide 31: Topic 9 Question
Which of the following should the NCS operator not expect of trained net members?
  To ask the NCS operator for permission to call another station
  To answer promptly when called by the NCS operator
  To follow established net protocols
  To rely exclusively on FCC call signs during net operations

## Slide 32: Topic 9 Question
Which if the following are appropriate to use in an emergency phone net?
  Plain English and 10-Codes
  Plain English and Prowords
  Q-Signals and Prowords
  Q-Signals and 10-Codes

## Slide 33: Topic 9 Question
Which is the best way to enlist the cooperation of the net?
  Immediately criticize net operators who make a mistake so that other operators will learn from the error
  Issue an order demanding the cooperation of all net operators
  Explain what you are doing in a calm and straightforward manner
  Immediately expel operators from the net who do not follow net protocol

## Slide 34: Any Questions Before Starting Topic 10?