## Slide 1: Training Volunteers
The ARRL
Introduction to Emergency Communication Course
EC-001 (2011)
Session Four
Notes: Make sure you have modified the Name and Date.
Display this screen as students are arriving for class.

## Slide 2: Reminder
Complete two DHS/FEMA Courses
    IS-100.b Introduction to ICS
    IS-700 National Incident Management System
      Http://training.fema.gov/IS/NIMS.asp
Notes: ARRL conditions!
The two ICS courses must be complete before taking the final exam.

## Slide 3: Session Four Topic
Session 1 – Topics 1, 2, 3, 4, 5a, 5b
Session 2 – Topics 6, 7a, 7b, 7c, 7d, 8, 9, 10
Session 3 – Topics 11, 12, 13, 14, 15
Session 4 – Topics 16, 17, 18, 19, 20
Session 5 – Topics 21, 22, 23, 24, 25, 26, 27
Session 6 – Topics 28, 29, Summary, Final Exam
Notes: The course requires a total of 18 hours.
If a student misses one class they can take a practice quiz for each lesson missed.
A student missing two sessions will be asked to take the course again.
A student missing the last session must wait for the next class and attend the final session for taking the exam again.
An exception would be two Field Examiners agreeing to give the exam at a mutually scheduled time.

## Slide 4: Topic 17 – Preparing for Deployment

## Slide 5: Prepared for What?
You never know which challenges an emergency situation will offer
Wide range of considerations
  including radio equipment
  power sources
  clothing and personal gear
  food and water,
  information
  specialized training

## Slide 6: Prepared for What?
No two deployments are the same, and each region offers its own specific challenges.
What is appropriate for rural Minnesota in January probably won't work for urban southern California in any season.
Goal is to help you think about ways to be prepared for your particular situation

## Slide 7: Jump Kits
It’s 3am..
Do you know where your equipment is?

## Slide 8: Jump Kits
Keep a kit of the items you need ready to go at a moment's notice, any time day or night, any condition
  Jump Kit
  Go Bag
Without a jump kit, you will leave something important at home, or bring items that will not do the job
Gathering and packing your equipment at the last moment wastes precious time
Think through each probable deployment ahead of time,
and range of situations you might encounter…

## Slide 9: Questions to Ask
Which networks will you need to join, and which equipment will you need to do so?
Will you need to be able to relocate quickly, or can you bring a ton of gear?
Will you be on foot, or near your vehicle?
Is your assignment at a fixed location or will you be mobile?
How long might you be deployed - less than 48 hours, up to 72 hours, or even a week or more?
Will you be in a building with reliable power and working toilets, or in a tent away from civilization? What sort of weather or other conditions might be encountered?
Where will food and water come from? Are sanitary facilities available?
Will there be a place to sleep?
Do you need to plan for a wide variety of possible scenarios, or only a few?
Can some items do “double duty” to save space and weight?

## Slide 10: Jump Kit Category
Divide jump kits into two categories
  Deployments under 24 hours
  One for up to 72 hours
Everyone has their own favorite list of items to keep in a jump kit
Notes: For deployments longer than 72 hours, many people will just add more of the items that they will use up, such as clothing, food, water, and batteries. Others may add a greater range of communication options and backup equipment as well.

## Slide 11: Jump Kit Idea List
Something to put it in
  One or more backpacks, suitcases, plastic storage tubs, etc.
  Package individual items in zip lock bags or plastic kitchen containers
Radios and Accessories
  Handheld VHF or dual-band radio (some people also like to bring a spare)
  Spare rechargeable batteries for handhelds
  Alkaline battery pack for handhelds
  Alkaline batteries
  Speaker mic and earphone for handhelds
  Battery chargers, AC and DC for handhelds

## Slide 12: Jump Kit Idea List (cont)
Radios and Accessories
  Mobile VHF or dual-band radio
  HF radio
  Multi-band HF antenna, tuner, heavy parachute cord or nylon mason's twine
  VHF/UHF gain antennas and adapters (roll-up J-Pole, mobile magnetic mount, etc)
  Coaxial feed lines, jumpers
  Ground rod, pipe clamp, and wire
Radios and Accessories
  AC power supplies for VHF.UHF mobile and HF radios, accessories
  Large battery source for VHF/UHF mobile and HF radios, with charger
  All related power, data, audio, and RF cables and adapters
  Small repair kit: hand tools, multi-meter, connectors, adapters, fuses, key parts

## Slide 13: Jump Kit Idea List (cont)
Radios and Accessories
  Materials for improvisation: wire, connectors, small parts, insulators, duct tape, etc.
  Photocopies of manuals for all equipment
  Headphones, for noisy areas and privacy with proper connector, adaptors
  Specialized gear for packet, ATV or other modes
Radios and Accessories
  Multi-band scanner, weather radio
  Personal cell phone, pager, spare batteries and chargers
  Pencils, legal pads, pencil sharpener

## Slide 14: Jump Kit Idea List (cont)
Personal Gear
  Clothing for the season, weather, and length of deployment
  Toilet kit: soap, razor, deodorant, comb, toilet paper
  Foul weather or protective gear, warm coats, hats, etc. as needed
  Sleeping bag, closed-cell foam pad, pillow, ear plugs
  High energy snacks
  Easily prepared dried foods that will store for long periods
  Eating and cooking equipment if needed
  Water containers, filled before departure
  First aid kit, personal medications and prescriptions for up to one week
  Money, including a large quantity of quarters for vending machines, tolls, etc.
  Telephone calling card

## Slide 15: Jump Kit Idea List (cont)
Information
  ID cards and other authorizations
  Copy of Amateur Radio license
  Frequency lists and net schedules
  Maps, both street and topographic
  Key phone numbers, email and internet addresses
  Contact information for other members in your group, EC, DEC, SEC, and others
  Copy of emergency plans
  Resource lists: who to call for which kinds of problems
  Log sheets, message forms

## Slide 16: Jump Kit Idea List (cont)
Operating Supplies
  Preprinted message forms
  Log sheets or books
  Standard forms used by the served agency
  Letter or legal size notepads
  Sticky notes
  Paper clips and rubber bands
  Blank envelopes
  Stapler, spare staples

## Slide 17: Sub-Dividing Your Kits
Quick deployment kit
  hand-held radio kit, personal essentials, in a large daypack
VHF/UHF, HF kits for fixed locations
Accessory and tool kit
Emergency power kit
Short and long term personal kits in duffel bags
Field kitchen and food box in plastic storage tubs
Field shelter kit (tents, tarps, tables, chairs, battery/gas lights) in plastic storage tubs
Notes: You may not want to pre-pack some items for reasons of expense or shelf life. Keep a checklist of these items in your jump kit so that you will remember to add them at the last minute.

## Slide 18: Pre-Planning
Where to go
What to do
  Which frequency should you check in on initially? Is there a "backup" frequency?
  If a repeater is out of service, which simplex frequency is used for the net?
  Which nets will be activated first?
  Should you report to a pre-determined location or will your assignment be made as needed?
Familiarize yourself with resources, requirements, and limitations for possible deployment locations

## Slide 19: Pre-Planning (cont)
Will you need a long antenna cable to get from your operating position to the roof?
Are antennas or cables permanently installed, or will you need to bring your own?
Will you be in one room with everyone else, or in a separate room?
Is there dependable emergency power to circuits at possible operating positions?
Does the building have an independent and dependable water supply?
Is there good cell phone or beeper coverage inside the building?
Can you reach local repeaters reliably with only a rubber duck antenna, or do you need an antenna with gain?
If the repeaters are out of service, how far can you reach on a simplex channel?
Will you need an HF radio to reach the net?

## Slide 20: Important Pre-Planning
Consider escape routes
  If you could be in the path of a storm surge or other dangerous condition, know all the possible routes out of the area
  If you will be stationed in a large building such as a school or hospital, find the fire exits, and learn which parking areas will be the safest for your vehicle

## Slide 21: Training & Education
The more you know, the more effective and valuable you will be
  Work within your own emcomm organization to get any additional training or information you might need
    American Red Cross offers self-study or classroom courses in mass care, damage assessment, and other areas that either directly involve or depend upon effective communication
    Federal Emergency Management Agency's Emergency Management Institute
  Participate in any drills or exercises offered
    ARRL's Field Day and Simulated Emergency Test

## Slide 22: Emergency Response Levels of Participation
Home
Neighbor
Neighborhood
Community
City
County
State
What do you need at each level?

## Slide 23: Summary
Any questions before the quiz?

## Slide 24
Time for a Quiz
Take 30 Seconds adjust your workspace

## Slide 25
30
Seconds

## Slide 26
20
Seconds

## Slide 27
10
Seconds

## Slide 28
9
Seconds

## Slide 29
8
Seconds

## Slide 30
7
Seconds

## Slide 31
6
Seconds

## Slide 32
5
Seconds

## Slide 33
4
Seconds

## Slide 34
3
Seconds

## Slide 35
2
Seconds

## Slide 36
1
Seconds

## Slide 37
Let's get started!

## Slide 38: Topic 17 Question
Of the following, which is the best reason for preparing a jump kit in advance?
  You will not leave something important at home or waste valuable time
  You are spared the added expense of shopping for something after an emergency arises
  You can be fully rested on the day of the emergency
  You can test the batteries on your hand held VHF before leaving home

## Slide 39: Topic 17 Question
Which of the following would you omit from a jump kit prepared for a 12-hour deployment?
  Hand held VHF or dual band radio
  Spare rechargeable batteries for the hand held radio
  High energy snacks
  Camp cot and tent

## Slide 40: Topic 17 Question
Among the following, which are the most important items of information to include in your jump kit?
  ID cards and other authorizations
  Field cookbook
  Automobile repair manual
  Instruction book for your chain saw

## Slide 41: Topic 17 Question
Among the following, which is the least important item of personal gear to include in your jump kit?
  Frequency lists and net schedules
  Contact information for other members of your group, EC, DEC and SEC
  Key phone numbers, email and Internet addresses
  A deck of playing cards

## Slide 42: Topic 17 Question
If you are assigned in advance to a particular location for emcomm operations, what is the least important thing to know in advance?
  The escape routes from the facility itself
  The regular business hours maintained at the facility
  The availability of radio equipment at the facility
  The location of your operating position and the planned location of the antenna

## Slide 43: Any Questions Before Starting Topic 18?